## Slide 2: Introduction
Emerging Environmental regulations directly impact the gas production and processing industry. The new regulations are intended to enhance protection of the environment and reduce human exposure to pollutants. This presentation will explore a few of the newer environmental regulations that directly impact the upstream and midstream natural gas industry. The discussion will focus on how analytical technology is being leveraged in support of these new regulations.

## Slide 3: Outline
Triggers for Development of New Environmental Guidelines
Examples of New and Emerging Environmental Guidelines
Technical Challenges Associated with New Guidelines
Leveraging Analytical Technology to Meet the Challenges
Summary

## Slide 4: Development of New Environmental Guidelines
  New scientific information becomes available.
  New or increased industrial activity creates a need for enhanced regulation.
  National or international trends influence regional environmental practice.
New Guidelines emerge when:

## Slide 5: New Environmental Guidelines
April 1, 2006, Alberta Environment
Amendments to the Air Monitoring Directive (AMD)
May 8, 2006, AEUB Directive 035
Baseline Water Well Testing Requirement for Coalbed Methane Wells Completed Above the Base of Groundwater Protection
July 10, 2006, AEUB Directive 039
Revised Program to Reduce Benzene Emissions from Glycol Dehydrators
October 31, 2006, AEUB Directive 044
Requirements for the Surveillance, Sampling, and Analysis of Water Production in Oil and Gas Wells Completed Above the Base of Groundwater Protection (BGWP)
June 2007, Alberta Environment
Alberta Tier 1 and Tier 2 Soil and Groundwater Remediation Guidelines

## Slide 6: Emerging Environmental Guidelines
2008?, Alberta Environment
Draft Alberta Tier 2 Vapour Inhalation Guidelines
- Standardized sample collection and analytical methods?
2008?, Alberta Environment
Draft Alberta Tier 2 Framework for Adjusting Eco-Contact Soil Criteria
- May require modified extraction procedures (cyclodextrin?)
2008?, Health Canada
Draft Benzene in Drinking Water Guideline
- Will likely impact groundwater criteria and potentially soil criteria

## Slide 7: Regional Guideline Development
New or emerging guidelines often trigger the development of new analytical technology.
Unique requirements are often driven by dominant industries or activity in a region.
  California = Methyl tertiary-butyl ether, MTBE
    Reformulated Gasoline
  Florida = Perchlorate
    Rocket Fuel

## Slide 8: Technical Challenges
Examples of unique environmental requirements related to the Canadian oil and gas industry.
  Sulfur Gases (H2S & SO2)
    Natural Gas Production and Processing
  Barium/Barite
    Drilling muds
  Diisopropanolamine (DIPA) and Sulfolane
    Gas Treating
  Methane
    Migrating Gas and Coalbed Methane

## Slide 9: Sulfur Gases (H2S and SO2)
Sulfur gases are not pollutants unique to Canada.
However, the extreme weather conditions found in western Canada disrupt most passive sampling technologies.
  The “Made in Canada” solution resulted in the development of an All Season – Climate insensitive passive sampler.

## Slide 10: Barium/Barite
Barite (barium sulfate, BaSO4) is a common component found in drilling muds.
Barite is insoluble and therefore less “bio-available”.
  Typically, soil quality guidelines are developed for trace metals rather than inorganic compounds.
  Alberta guidelines were established following extensive research on the impact and risk associated with high concentrations of barite.
  Resulting in more appropriate environmental protection.

## Slide 11: Diisopropanolamine (DIPA) and Sulfolane
Sulfolane and DIPA are commonly used as gas treating solvents.
No existing environmental guidelines could be found in any jurisdiction.
  Guideline development required some fundamental research.
  Toxicity, Biota & Mammalian?
  Fate and Transport?
2006

## Slide 12: Methane
Not generally considered a pollutant.
Methane is a significant greenhouse gas.
Migrating subsurface natural gas can deplete O2 in the surrounding soil.
Migration of natural gas into groundwater aquifers must be avoided.

## Slide 13
11/28/06 KM,U of A
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Natural Gas Composition
The challenge: natural gas composition of shallow gas is not unique.
Isotopic data is usually required to distinguish between compositionally similar natural gases.

## Slide 15: Changing Isotope Signature With Depth

## Slide 16: EUB Directive 35
Baseline Water Well Testing Requirement for Coalbed Methane Wells Completed Above the Base of Groundwater Protection
Effective May 1, 2006, baseline testing of water wells is mandatory for companies wanting to drill or recomplete a well to produce coalbed methane (CBM) above the base of groundwater protection (BGWP). The testing will gather background information on the water well’s production capability and water quality.

## Slide 17: Current Challenges
New Alberta Tier 1 and Tier 2 Soil and Groundwater Remediation Guidelines
  Several New additions:
    Aniline, bis(chloromethyl)ether, dichlorobenzidene, DIPA, Ethylene Glycol, Hexachlorobutadiene, methylmethacrylate, MTBE, nonylphenol, sulfolane, aliphatic/aromatic petroleum fractions.
  Several very low guideline values
    Polyaromatic hydrocarbons (PAH’s)
    Halogenated volatile compounds

## Slide 18: Summary
New environmental regulations will continue to emerge.
Some new regulations will be in response to oil & gas activity.
Direct involvement and support of guideline related research ensures appropriate and scientifically defensible regulations.
Regional regulations can be unique. The unique character can come from:
  A unique compound (pollutant)
  Unique fate and transport
  Unique environment
Western Canada has developed a history of cooperation between government, industry, service providers and academic institutions.

## Slide 19: Questions and Discussion