## Slide 1
Gerry Goobie, P.Eng.
Purvin & Gertz, Inc.
(403) 984-2205
Presented to:
GPA Canada/PJVA
Annual Joint Conference
November 12, 2008
The NGL Inquiry
Notes: <number>

## Slide 2: ABOUT THIS PRESENTATION
<number>
This analysis has been prepared for the sole benefit of the Client. Neither the analysis nor any part of the analysis shall be provided to third parties without the written consent of Purvin & Gertz. Any third party in possession of the analysis may not rely upon its conclusions without the written consent of Purvin & Gertz. Possession of the analysis does not carry with it the right of publication.
Purvin & Gertz conducted this analysis utilizing reasonable care and skill in applying methods of analysis consistent with normal industry practice. All results are based on information available at the time of review. Changes in factors upon which the review is based could affect the results. Forecasts are inherently uncertain because of events or combinations of events that cannot reasonably be foreseen including the actions of government, individuals, third parties and competitors. NO IMPLIED WARRANTY OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE SHALL APPLY.
Some of the information on which this analysis is based has been provided by others. Purvin & Gertz has utilized such information without verification unless specifically noted otherwise. Purvin & Gertz accepts no liability for errors or inaccuracies in information provided by others.
Notes: <number>

## Slide 3: DISCLAIMER
<number>
The NGL Inquiry and NGTL Jurisdiction are still before the EUB and NEB
  Therefore not appropriate to repeat arguments here
Full Disclosure
  I acted for the Straddle Plant Group
Any opinions are Gerry Goobie’s opinions
  Not SPG’s opinions
  Not P&G’s opinions
I am not a lawyer
  Not legal opinions
The NGL business is not straight forward
  There is a lot to this story and I will only discuss a portion of it
Notes: <number>

## Slide 4: Outline
<number>
Purvin & Gertz Overview
Natural Gas Supply and Demand
NGL Extraction Convention History
NGL Inquiry Issues
Notes: <number>

## Slide 5: Purvin & Gertz Overview
<number>
Independent consulting firm founded in 1947
Consultant owned – independent of any engineering firm or process licensor
Serving clients involved in exploration, production, processing, transportation, distribution, marketing and consumption of:
  Natural Gas
  NGL
  Crude Oil
  Petroleum Products
Also serving clients in the financial community, law firms, regulatory bodies and government agencies
Located in 8 offices worldwide…
Notes: <number>
3

## Slide 6: A Global Network To Serve Clients Worldwide
<number>
Houston
Calgary
London
Buenos Aires
Singapore
Los Angeles
Moscow
Dubai
Notes: <number>

## Slide 7: Canadian Natural Gas Supply and Demand
<number>
<number>
Notes: <number>

## Slide 8: Western Canada Natural Gas Supply
<number>
Conventional natural gas production is declining
  Dramatic drop in gas directed drilling in 2007
  Total wells drilled: >23,000 in 06; 18,600 in 07; expected 14,500 in 08
  Drilling shifting to BC (deep, sour, liquids rich) and Saskatchewan (shallow, sweet, dry)
Coal bed methane, shale gas and Northern gas are expected to partially offset supply shortfall
Notes: <number>

## Slide 9: Western Canada Drilling Rigs

## Slide 10: Western Canada Natural Gas Supply
<number>
Coal bed methane
  CBM contains no NGL (primarily PSAC 3 & 5)
  Will it be segregated from rich gas streams?
Shale Gas
  Tremendous land interest in Montney and Horn River
  Gas quality is not clear
  Lack of infrastructure will constrain development
Arctic Gas
  Both Mackenzie and Alaska are in regulatory processes
  Mackenzie gas is relatively lean (after IAF)
  Alaska gas is relatively rich
  Significant interest in attracting Arctic gas to Alberta hub
Notes: <number>

## Slide 11: Canadian Natural Gas Issues
<number>
<number>
Declining supply and increased domestic demand will reduce exports
NGL Production will decline
Prices will be volatile
Notes: <number>

## Slide 12: Frac Spread - The How Much Question

## Slide 13: NGL Inquiry History
<number>
Pre 1985 Deregulation
  Aggregators
  Long term contracts underpinned infrastructure
  Straddles built at export points
Post 1985 Deregulation
  Pipeline expansions
  Ethane wars
  Separation of receipt and delivery service
  Growth of storage
  Development of NIT market
Notes: <number>

## Slide 14: NGL Inquiry History (cont’d)
<number>
Gulf Strachan
  First to raise the ownership issue
  Sidestreaming allowed with conditions
Solex Harmattan
  3rd party sidestreaming disallowed
  NGTL instructed to sort it all out
NECTF
  Lots of effort but didn’t sort out anything
Taylor Harmattan
  Proposed Co-streaming
Notes: <number>

## Slide 15: NGL Inquiry Issues
<number>
Current Convention
Ethane Policy
Perceived Inequities
Sidestreaming and Co-streaming
Lean Gas Streaming
Ex-Alberta Gas Considerations
Consideration of Alternatives & Impacts
Component Tracking
NGL on ATCO Pipelines & AltaGas
EUB Reg Facilities on non-EUB Reg Pipelines
Notes: <number>

## Slide 16: The Current Convention
<number>
It is simple and it works
The controversy is whether it is “Fair”
  The fairness complaint is based on a belief that “producers” are not getting value for their NGL
  Some important facts:
    Receipt Shipper ≠ Producer
    > 750 producers
    ~ 130 receipt shippers on NGTL
    20 receipt shippers control >75% of receipt volume
  Realizing NGL value requires investment in processing facilities
    Otherwise, it’s just gas
Notes: <number>

## Slide 17: Ethane Policy
<number>
The Ethane Policy was developed as a result of the “Ethane Wars” in the late 1980’s
Policy expired June 30, 2008
Doesn’t appear to be much enthusiasm for a new policy, i.e. let the market decide
Notes: <number>

## Slide 18: Perceived Inequities
<number>
Perceived Inequities include:
  HV < or > Common Stream
  Gas receipts downstream of straddles
  Double Dipping
  Receipt shippers do not appear to get NGL value
NECTF could not agree whether the perceived inequities were real or material
Notes: <number>

## Slide 19: Sidestreaming and Co-Streaming
<number>
Doesn’t appear to be much support for sidestreaming
Some have suggested that each co-streaming application should be reviewed on its own merits
One important issue is excess capacity
  The big field plants are at about 50% capacity
  The straddles are at about 2/3 capacity
Co-streaming could make sense if there is gas that is not being processed otherwise
Notes: <number>

## Slide 20: Lean Gas Streaming and ex-Alberta Gas
<number>
Lean Gas Streaming
  AUC gives an indication in the NCC ruling
  Lean Gas Streaming is probably a good idea
  Industry needs to sort out the details
Ex-Alberta Gas Considerations
  If and when Arctic gas flows, then it is expected to flow through Alberta
    Mackenzie and Alaska (TCPL and Denali)
  There is no impediment to making commercial processing arrangements at that time
Notes: <number>

## Slide 21: Alternatives and Impacts
<number>
Existing Convention versus Alternatives
  Cost/benefit of change
  Does the alternative resolve Perceived Inequities?
  Does the alternative create new inequities?
Current options to get value for NGL are:
  Process in field before NGTL receipt
  Take out export delivery service and contract with straddle plants
  Build or buy straddle capacity
Notes: <number>

## Slide 22: Receipt Point Contracting - NEXT
<number>
Receipt Point Contracting (RPC) is suggested as an alternative
  The idea behind RPC is to allocate entitlement to NGL at receipt points based on gas composition and then have a mechanism to reallocate at extraction plants
NGTL proposed NEXT model
NEXT is a big allocation algorithm
  It generates a volume number based on gas receipts, compositions and prices in a previous period
  Everyone gets reduced NGL due to intra-Alberta deliveries
Notes: <number>

## Slide 23: Receipt Point Contracting - NEXT
<number>
Several issues arise:
  What exactly is being allocated?
    NGL and rich gas are not homogeneous commodities on NGTL
    Requires separating NGL entitlement from physical gas flow
  Ownership in not clear
  Should allocate ALL the ins and outs
    Component tracking
  It will require tariff changes
Notes: <number>

## Slide 24: Other Alternatives
<number>
Equalization
  Didn’t get much discussion
  It has worked for many years in crude oil
  It could resolve the HV inequity
  Big issue would be setting the EQ value
Notes: <number>

## Slide 25: Other Pipelines and Facilities
<number>
NGL extraction is different on other pipelines
The issue didn’t get a lot of discussion
Other pipelines and facility owners are generally opposed to changing their situation
Notes: <number>

## Slide 26: Conclusions
<number>
The NGL Business is not straightforward
Therefore …
Notes: <number>

## Slide 27: Hire a Good Guide. It Will Be Worth It!
Notes: <number>
3